NOVA-4710

SOCKET 478 (Mobile) Pentium 4 / Celeron with Ethernet LAN / LCD AGP4X VGA Embedded Board

User Manual Version 1.0

December, 12, 2003

Copyright 2003 by ICP Electronics Inc.  All Rights Reserved.

Copyright Notice

The information in this document is subject to change without prior notice in order to improve reliability, design and function and does not represent a commitment on the part of the manufacturer.

In no event will the manufacturer be liable for direct, indirect, special, incidental, or consequential damages arising out of the use or inability to use the product or documentation, even if advised of the possibility of such damages.

This document contains proprietary information protected by copyright.  All rights are reserved.  No part of this manual may be reproduced by any mechanical, electronic, or other means in any form without prior written permission of the manufacturer.

Trademarks

NOVA-4710 is a registered trademark of ICP Electronics Inc. IBM PC is a registered trademark of International Business Machines Corporation.  Intel is a registered trademark of Intel Corporation.  Other product names mentioned herein are used for identification purposes only and may be trademarks and/or registered trademarks of their respective companies.

Support

Any questions regarding the product or the content of this manual please email us at: support@iei.com.tw

Table of Contents

1.	Introduction	5

1.1	Specifications	6

1.2	Package Contents	8

2.	Installation	9

2.1	NOVA-4710 Layout	9

2.2	Unpacking Precautions	10

2.3	CompactFlash Master (close)/Slave (open) setting	10

2.4	LCD Power setting	11

2.5	CPU Voltage Setting	11

2.6	Clear CMOS	11

2.7	COM1/2 Port RI and Voltage select	12

2.8	COM3/4 Port RI and Voltage select	12

2.9	COM5/6 Port RI and Voltage select	13

2.10	Keyboard Use Selection	13

3.	Connection	14

3.1	PCI E-IDE Disk Drive Connector	15

3.2	IO Connector	17

3.3	COM3/4/5/6 Port Connectors	18

3.4	External Switches and Indicators	18

3.5	USB Port Connectors	19

3.6	IrDA Infrared Interface Port	19

3.7	Fan Connectors	19

3.8	LAN State LED Connectors	20

3.9	VGA Connector	20

3.10	Audio Connector	20

3.11	ATX-12V Power Connector	21

3.12	Digital INPUT/OUTPUT Connector	21

3.13	LVDS (CN4) LCD & Inverter (CN5) Connector	22

4.	Award BIOS Setup	23

4.1    Introduction	23

4.2    Starting Setup	23

4.3    Using Setup	24

4.4    Main Menu	25

4.5    Standard CMOS Setup	27

4.6    Advanced BIOS Features	30

4.7    Advanced Chipset Features	33

4.8    Integrated Peripherals	36

4.9    Power Management Setup	39

4.10    PnP/PCI Configuration Setup	41

4.11    PC Health Status	43

4.12    Frequency/Voltage Control	44

4.13    Defaults Menu	45

4.14    Supervisor/User Password Setting	46

4.15    Exit Selecting	47

Appendix A: Watchdog Timer	48

Appendix B: I/O Address Map	49

Appendix C: How to use Wake-Up Function	51

# Introduction

Thank you for choosing NOVA-4710 SOCKET 478 (Mobile) Pentium 4 / Celeron Single Board Computer.  NOVA-4710 board is a 5.25” embedded form factor board equipped with high performance processor and multi-mode I/O designed for the system manufacturers, integrators, or VARs with reliable and quality performance at a reasonable price.

In addition, the VGA controller of NOVA-4710 Built-in AGP4X VGA (Intel 852GM/GME) has 3D graphics capability, which provides up to 1920x1440x16-color resolution. The onboard VGA shares 32MB(max) system DDR-SDRAM.

An advanced high performance super AT I/O chip–ITE IT8712 & Fintek F81216D are used in the NOVA-4710 board. On-chip UARTs are compatible with NS16C550. The parallel port and IDE interface are compatible with IBM PC/AT architecture.

NOVA-4710 has built-in (ICH4) 10/100. They are fully integrated 10BASE-T/100BASE-TX LAN solution with high performance networking functions with low power consumption.

NOVA-4710 uses Intel 852GM/GME chipsets which are 100% software compatible and are of PCI 2.2 standard.

## Specifications

| CPU (PGA 478) | Intel (Mobile) Pentium 4 / Celeron Processor, supports 400/533 MHz FSB |
| --- | --- |
| Bus speed | PCI: 33 MHz |
| DMA channels | 7 |
| Interrupt levels | 15 |
| Chipset | INTEL 852GM/GME (GMCH) |
| Real-time clock | INTEL 82801DB (ICH4) |
| System memory | One 184-pin DIMM socket to support DDR 200/266/333 SDRAM. The maximum memory is up to 1 GB. |
| ATA/100 IDE interface | Up to four PCI Enhanced IDE hard drives. The ATA/100 IDE can handle data transfer up to 100 MB/s. |
| Serial ports | COM1, COM2, COM3, COM4, COM5, COM6 with 16C550 UART (or compatible) with 16-byte FIFO buffer. Supports up to 115.2Kbps. |
| Bi-directional parallel port | Configurable to LPT1, or disabled. Supports EPP/ECP/SPP |
| Hardware monitor | Built in to monitor power supply voltage and fan speed status |
| IrDA port | Supports Serial Infrared (SIR) and Amplitude Shift Keyed IR (ASKIR) interface |
| USB port | Supports 4 USB 2.0 ports for future expansion |
| Watchdog timer | Software Programmable Reset generated when CPU does not periodically trigger the timer. Your can use INT15 to control the watchdog and generate a system reset. |
| VGA controller | Built-in AGP2.0 4X 3D graphics engine. Share system DDR SDRAM 32MB(max). Flat panel on-chip 852GM(852GME) Supports 18bit/24bit single pixel or 36bit/48bit dual pixel color LVDS TFT LCD. |
| Ethernet | ICH4 Fast Ethernet controllers, IEEE 802.3u Auto-Negotiation support for 10BASE-T/ 100BASE-TX standard. |
| Keyboard and PS/2 mouse | A 6-pin header connector is located on board for easy connection to keyboard. And I/O connector to PS/2 mouse. |
| Digital input/output | It provide with 4-bit digital input/output (+12V level). Your can use I/O PORT 201H to control it. |
| Audio | AC’97 Audio CODEC. |
| Compact flash | It can be used (IDE2) with a passive adapter (True IDE Mode) in a Type I Socket. |
| Power consumption | (Pentium 4-M (mobile CPU): 2.4GHz, 512MB DDR266-SDRAM) +5V @ 4.0A, +12V @ 4.00A. Recommended: 300-watt power supply or higher |
| Operating temperature | 0 ℃ ~ 60 ℃ (*CPU needs Cooler & silicone heat sink paste*) |

WARNING:

- Run the processor only when the heat sink (cooler) is properly and firmly attached.

- Please use ATX-12V Power Connector (CN2) to supply power to the CPU.

## Package Contents

In addition to this User's Manual, the NOVA-4710 package includes the following items:

- NOVA-4710 single board computer

- CD Drivers

If any of these items are missing or damaged, please contact the dealer from whom you purchased this product.  Save the shipping materials and carton in case you want to ship or store the product in the future.

# Installation

## NOVA-4710 Layout

## Unpacking Precautions

Some components on NOVA-4710 SBC are very sensitive to static electric charges and can be damaged by a sudden rush of power.  To protect it from unintended damage, be sure to follow these precautions:

- Ground yourself to remove any static charge before touching your NOVA-4710 SBC.  You can do it by using a grounded wrist strap at all times or by frequently touching any conducting materials that is connected to the ground.

- Handle your NOVA-4710 SBC by its edges.  Don’t touch IC chips, leads or circuitry if not necessary.

- Do not plug any connector or jumper while the power is on.

Table of Jumpers

| Label | Function |
| --- | --- |
| JP1 | CompactFlash Master / Slave setting |
| JP2 | LCD Power setting |
| JP3 | CPU voltage setting |
| JP4 | CMOS state setting |
| JP5 | COM1/2 Port RI and Voltage select |
| JP6 | COM3/4 Port RI and Voltage select |
| JP7 | COM5/6 Port RI and Voltage select |
| CN17 | Keyboard Use Selection |

## CompactFlash Master (close)/Slave (open) setting

Set the operating mode of CompactFlash disk. This is similar to the operation of hard disk.

| JP1 | Description |
| --- | --- |
| OPEN | Slave |
| Close | Master |

## LCD Power setting

This jumper is for the setting of LCD panel voltage.

| JP2 | Description |
| --- | --- |
| 1-2 | +3.3V |
| 2-3 | +5V |

## CPU Voltage Setting

This jumper is for the setting of CPU voltage.

| JP3 | 1-2 | 3-4 | 5-6 | 7-8 | 9-10 |
| --- | --- | --- | --- | --- | --- |
| 1.100 | OPEN | OPEN | OPEN | OPEN | Close |
| 1.125 | OPEN | OPEN | OPEN | Close | OPEN |
| 1.150 | OPEN | OPEN | OPEN | Close | Close |
| 1.175 | OPEN | OPEN | Close | OPEN | OPEN |
| 1.200 | OPEN | OPEN | Close | OPEN | Close |
| 1.225 | OPEN | OPEN | Close | Close | OPEN |
| 1.250 | OPEN | OPEN | Close | Close | Close |
| 1.275 | OPEN | Close | OPEN | OPEN | OPEN |
| 1.300 | OPEN | Close | OPEN | OPEN | Close |
| 1.325 | OPEN | Close | OPEN | Close | OPEN |
| 1.350 | OPEN | Close | OPEN | Close | Close |
| 1.375 | OPEN | Close | Close | OPEN | OPEN |
| 1.400 | OPEN | Close | Close | OPEN | Close |
| 1.425 | OPEN | Close | Close | Close | OPEN |
| 1.450 | OPEN | Close | Close | Close | Close |
| 1.475 | Close | OPEN | OPEN | OPEN | OPEN |
| 1.500 | Close | OPEN | OPEN | OPEN | Close |
| 1.525 | Close | OPEN | OPEN | Close | OPEN |
| 1.550 | Close | OPEN | OPEN | Close | Close |
| 1.575 | Close | OPEN | Close | OPEN | OPEN |
| 1.600 | Close | OPEN | Close | OPEN | Close |
| 1.625 | Close | OPEN | Close | Close | OPEN |
| 1.650 | Close | OPEN | Close | Close | Close |
| 1.675 | Close | Close | OPEN | OPEN | OPEN |
| 1.700 | Close | Close | OPEN | OPEN | Close |
| 1.725 | Close | Close | OPEN | Close | OPEN |
| 1.750 | Close | Close | OPEN | Close | Close |
| 1.775 | Close | Close | Close | OPEN | OPEN |
| 1.800 | Close | Close | Close | OPEN | Close |
| 1.825 | Close | Close | Close | Close | OPEN |
| 1.850 | Close | Close | Close | Close | Close |

## Clear CMOS

To clear the CMOS data, close the JP4 (2-3) for about 3 seconds, then open it again.

- JP4		: Clear CMOS  (Reserved Function)

| JP4 | Description |
| --- | --- |
| 1-2 | Normal Operation |
| 2-3 | Clear CMOS Setup |

WARNING:

When you change the power supply between ATX and AT, clear CMOS (Power On) first.  Otherwise, the CPU Board may fail to boot up.

## COM1/2 Port RI and Voltage select

JP5: Set pin 9 of COM1 as signal RI or voltage source

| JP5 | DESCRIPTION |
| --- | --- |
| 9-11 | COM1 RI Pin Use RI |
| 7-9 | COM1 RI Pin Use Voltage |

JP5: Set pin 9 of COM2 as signal RI or voltage source

| JP5 | DESCRIPTION |
| --- | --- |
| 10-12 | COM2 RI Pin Use RI |
| 8-10 | COM2 RI Pin Use Voltage |

JP5: Set pin 9 of COM1 as +5V or 12V

| JP5 | DESCRIPTION |
| --- | --- |
| 1-3 | COM1 RI Pin Use Voltage +5V |
| 3-5 | COM1 RI Pin Use Voltage +12V |

JP5: Set pin 9 of COM2 as +5V or 12V

| JP5 | DESCRIPTION |
| --- | --- |
| 2-4 | COM2 RI Pin Use Voltage +5V |
| 4-6 | COM2 RI Pin Use Voltage +12V |

## COM3/4 Port RI and Voltage select

JP6: Set pin 9 of COM3 as signal RI or voltage source

| JP6 | DESCRIPTION |
| --- | --- |
| 9-11 | COM3 RI Pin Use RI |
| 7-9 | COM3 RI Pin Use Voltage |

JP6: Set pin 9 of COM4 as signal RI or voltage source

| JP6 | DESCRIPTION |
| --- | --- |
| 10-12 | COM4 RI Pin Use RI |
| 8-10 | COM4 RI Pin Use Voltage |

JP6: Set pin 9 of COM3 as +5V or 12V

| JP6 | DESCRIPTION |
| --- | --- |
| 1-3 | COM3 RI Pin Use Voltage +5V |
| 3-5 | COM3 RI Pin Use Voltage +12V |

JP6: Set pin 9 of COM4 as +5V or 12V

| JP6 | DESCRIPTION |
| --- | --- |
| 2-4 | COM4 RI Pin Use Voltage +5V |
| 4-6 | COM4 RI Pin Use Voltage +12V |

## COM5/6 Port RI and Voltage select

JP7: Set pin 9 of COM5 as signal RI or voltage source

| JP7 | DESCRIPTION |
| --- | --- |
| 9-11 | COM5 RI Pin Use RI |
| 7-9 | COM5 RI Pin Use Voltage |

JP7: Set pin 9 of COM6 as signal RI or voltage source

| JP7 | DESCRIPTION |
| --- | --- |
| 10-12 | COM6 RI Pin Use RI |
| 8-10 | COM6 RI Pin Use Voltage |

JP7: Set pin 9 of COM5 as +5V or 12V

| JP7 | DESCRIPTION |
| --- | --- |
| 1-3 | COM5 RI Pin Use Voltage +5V |
| 3-5 | COM5 RI Pin Use Voltage +12V |

JP7: Set pin 9 of COM6 as +5V or 12V

| JP7 | DESCRIPTION |
| --- | --- |
| 2-4 | COM6 RI Pin Use Voltage +5V |
| 4-6 | COM6 RI Pin Use Voltage +12V |

## Keyboard Use Selection

The NOVA-4710 provides CN17 keyboard connector or optional keyboard output for IO connector.

CN17 : 6-pin Header  Mouse Connector

| CN17 | DESCRIPTION |
| --- | --- |
| 2-3 , 4-5 | KB use for IO connector |
| OPEN | KB use for CN20 |

# Connection

This chapter describes how to connect peripherals, switches and indicators to the NOVA-4710 board.

Table of Connectors

| LABEL | FUNCTION |
| --- | --- |
| CN1 | Power supply to Main board Connector |
| CN2 | ATX-12V CPU Power Source |
| CN3 | VGA 10-pin Connector |
| CN4 & CN5 | LVDS panel & Inverter Connectors |
| CN6/19 | COM3/4 Port Connectors |
| CN7 | Digital INPUT/OUTPUT Connector |
| CN9/10/11 | AUDIO MIC-IN, LINE-IN, LINE-OUT Connector |
| CN12 | LAN State LED Connectors |
| CN13 | ATX BUTTON (Power ON) Switch |
| CN15 | External Switches and Indicators |
| CN18/27 | Fan Connectors |
| CN20 | IO Connector |
| CN21 | USB Connectors |
| CN25/26 | COM5/6 Port Connectors |
| IR1 | IrDA Connector |
| IDE1 | Primary IDE Connector |
| IDE2/CF1 | Secondary IDE Connector |

## PCI E-IDE Disk Drive Connector

You can attach four IDE (Integrated Device Electronics) hard disk drives on two channels.  These connectors support Ultra-DMA100 IDE devices.  It is recommended to connect Non-DMA100 devices to the secondary IDE connector.

IDE1 : Primary IDE Connector (Pitch 2.54 mm)

IDE2 : Secondary IDE Connector (Pitch 2.0 mm)

- IDE Interface Connector

| PIN | Description | PIN | Description |
| --- | --- | --- | --- |
| 1 | RESET# | 2 | GROUND |
| 3 | DATA 7 | 4 | DATA 8 |
| 5 | DATA 6 | 6 | DATA 9 |
| 7 | DATA 5 | 8 | DATA 10 |
| 9 | DATA 4 | 10 | DATA 11 |
| 11 | DATA 3 | 12 | DATA 12 |
| 13 | DATA 2 | 14 | DATA 13 |
| 15 | DATA 1 | 16 | DATA 14 |
| 17 | DATA 0 | 18 | DATA 15 |
| 19 | GROUND | 20 | N/C |
| 21 | N/C | 22 | GROUND |
| 23 | IOW# | 24 | GROUND |
| 25 | IOR# | 26 | GROUND |
| 27 | N/C | 28 | BALE – DEFAULT |
| 29 | N/C | 30 | GROUND – DEFAULT |
| 31 | INTERRUPT | 32 | IOCS16# - DEFAULT |
| 33 | SA1 | 34 | N/C |
| 35 | SA0 | 36 | SA2 |
| 37 | HDC CS0# | 38 | HDC CS1# |
| 39 | HDD ACTIVE# | 40 | GROUND |
| 41 | +5V | 42 | +5V |
| 43 | GROUND | 44 | N/C |

Note: Pins 41~44 are applicable for IDE2 only.

The NOVA-4710 includes a slot for a Compact Flash Storage Card  in IDE Mode(Using IDE2).

CF1 : Compact Flash Storage Card Socket

| PIN | DESCRIPTION | PIN | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | GROUND | 26 | CARD DETECT1 |
| 2 | D3 | 27 | D11 |
| 3 | D4 | 28 | D12 |
| 4 | D5 | 29 | D13 |
| 5 | D6 | 30 | D14 |
| 6 | D7 | 31 | D15 |
| 7 | CS1# | 32 | CS3# |
| 8 | N/C | 33 | N/C |
| 9 | GROUND | 34 | IOR# |
| 10 | N/C | 35 | IOW# |
| 11 | N/C | 36 | OBLIGATORY TO PULL HIGH |
| 12 | N/C | 37 | IRQ15 |
| 13 | VCC | 38 | VCC |
| 14 | N/C | 39 | MASTER/SLAVE |
| 15 | N/C | 40 | N/C |
| 16 | N/C | 41 | RESET# |
| 17 | N/C | 42 | IORDY |
| 18 | A2 | 43 | N/C |
| 19 | A1 | 44 | OBLIGATORY TO PULL HIGH |
| 20 | A0 | 45 | ACTIVE# |
| 21 | D0 | 46 | PDIAG# |
| 22 | D1 | 47 | D8 |
| 23 | D2 | 48 | D9 |
| 24 | N/C | 49 | D10 |
| 25 | CARD DETECT2 | 50 | GROUND |

## IO Connector

CN20 : IO Connector-LAN, COM1.2, Printer, KB/MS, DIO...

| PIN | DESCRIPTION | PIN | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | EAROUT_L | 2 | DIO_IN00 |
| 3 | DIO_OUT01 | 4 | DIO_OUT00 |
| 5 | COM4_DTR | 6 | COM4_DSR |
| 7 | COM4_RTS | 8 | COM4_CTS |
| 9 | EAROUT_R | 10 | COM4_SOUT |
| 11 | COM2_CTS | 12 | COM2_RI |
| 13 | COM2_DSR | 14 | COM2_RTS |
| 15 | COM2_SOUT | 16 | COM2_DTR |
| 17 | COM2_DCD | 18 | COM2_SIN |
| 19 | COM1_CTS | 20 | COM1_RI |
| 21 | COM1_DSR | 22 | COM1_RTS |
| 23 | COM1_SOUT | 24 | COM1_DTR |
| 25 | COM1_DCD | 26 | COM1_SIN |
| 27 | K/B_CLK | 28 | K/B_DATA |
| 29 | MOUSE_CLK | 30 | MOUSE_DATA |
| 31 | USB3+ |  | USB3- |
| 33 | USB2+ |  | USB2- |
| 35 | COM4_SIN | 36 | PRT_STB# |
| 37 | PRT_D0 | 38 | PRT_D1 |
| 39 | PRT_D2 | 40 | PRT_D3 |
| 41 | PRT_D4 | 42 | PRT_D5 |
| 43 | PRT_D6 | 44 | PRT_D7 |
| 45 | PRT_ACK# | 46 | PRT_PE |
| 47 | PRT_BUSY | 48 | PRT_SLCT |
| 49 | PRT_AED# | 50 | PRT_ERR# |
| 51 | PRT_INIT# | 52 | PRT_SLIN |
| 53 | LAN_L78 | 54 | LAN_L78 |
| 55 | LAN_L45 | 56 | LAN_L45 |
| 57 | LAN_TX+ | 58 | LAN_RX+ |
| 59 | LAN_TX- | 60 | LAN_TX+ |

## COM3/4/5/6 Port Connectors

- CN6 : COM3 10-pin header

- CN19 : COM4 10-pin header

- CN25 : COM5 10-pin header

- CN26 : COM6 10-pin header

| PIN | Description | PIN | Description |
| --- | --- | --- | --- |
| 1 | DATA CARRIER DETECT (DCD) | 2 | DATA SET READY (DSR) |
| 3 | RECEIVE DATA (RXD) | 4 | REQUEST TO SEND (RTS) |
| 5 | TRANSMIT DATA (TXD) | 6 | CLEAR TO SEND (CTS) |
| 7 | DATA TERMINAL READY (DTR) | 8 | RING INDICATOR (RI) |
| 9 | GROUND | 10 | NC |

## External Switches and Indicators

There are several external switches and indicators for monitoring and controlling the CPU board.  All the functions are in CN15 connector.

- CN15: External Switches and Indicators

|  | PIN | Description | PIN | Description |  |
| --- | --- | --- | --- | --- | --- |
| Power LED | 1 | +5V | 2 | Speaker + | Speaker |
|  | 3 | N/C | 4 | N/C |  |
|  | 5 | GND | 6 | N/C |  |
| KEYLOCK | 7 | KEYLOCK PIN1 | 8 | Speaker - |  |
|  | 9 | KEYLOCK PIN2 | 10 | Reset PIN1 | Reset Button |
|  | 11 | GND | 12 | Reset PIN2 |  |
| HDD LED | 13 | HDD LED+ | 14 | HDD LED - | HDD LED |

- CN13: 2-pin Header ATX POWER BUTTON Connector

| PIN | Description |
| --- | --- |
| 1 | BUTTON PIN 1 |
| 2 | BUTTON PIN 2 |

## USB Port Connectors

NOVA-4710 provides 4 built-in USB2.0 ports for new I/O bus expansion.

| CN21 |
| --- |
| PIN | Description | PIN | Description |
| 1 | VCC | 2 | GROUND |
| 3 | DATA0- | 4 | DATA1+ |
| 5 | DATA0+ | 6 | DATA1- |
| 7 | GROUND | 8 | VCC |

## IrDA Infrared Interface Port

NOVA-4710 has a built-in IrDA port which supports Serial Infrared (SIR) or Amplitude Shift Keyed IR (ASKIR) interface.  To use the IrDA port, configure SIR or ASKIR model in the BIOS under Peripheral Setup COM2.  The normal RS-232 COM 2 will be disabled.

- IR1: IrDA Connector

| PIN | Description |
| --- | --- |
| 1 | VCC |
| 2 | N/C |
| 3 | IR-RX |
| 4 | Ground |
| 5 | IR-TX |
| 6 | VCC |

## Fan Connectors

NOVA-4710 provides two CPU cooling fan connectors which can supply 12V/500mA to the cooling fan.  All connectors have the same pin assignments and provide a "rotation" pin to get rotation signals from fans and notice the system.  So the system BIOS can recognize the fan speed.  Please note that only specified fan can issue the rotation signals.

- CN18/27 : Fan Connector

| PIN | Description |
| --- | --- |
| 1 | Rotation Signal |
| 2 | +12V |
| 3 | Ground |

## LAN State LED Connectors

NOVA-4710 is equipped with LAN1 10/100-TX Ethernet controllers. There are two LED on the connector indicating the status of LAN.  The pin assignments are listed below:

- CN12 : LAN State LED Connector

| PIN | Description |
| --- | --- |
| 1-2 | LINK |
| 3-4 | ACTIVE |

## VGA Connector

NOVA-4710 has a built-in 10-pin VGA connector directly connected to your CRT monitor.

- CN3 : 10-pin Female Connector

| PIN | Description | PIN | Description |
| --- | --- | --- | --- |
| 1 | RED | 2 | DDC DAT |
| 3 | GREEN | 4 | DDC CLK |
| 5 | BLUE | 6 | GROUND |
| 7 | HSYNC | 8 | GROUND |
| 9 | VSYNC | 10 | GROUND |

## Audio Connector

NOVA-4710 has a built-in AC’97 AUDIO CODEC connector directly connected to your MIC-IN & LINE-IN & LINK-OUT.

- CN9 : MIC Input Connector

| 1 | N/C |
| --- | --- |
| 2 | GROUND |
| 3 | GROUND |
| 4 | MIC IN |

- CN10 : LINE Input Connector

| 1 | LEFT LINE IN SIGNAL |
| --- | --- |
| 2 | GROUND |
| 3 | GROUND |
| 4 | RIGHT LINE IN SIGNAL |

- CN11 : LINE Output Connector

| 1 | LEFT SPEAKER OUT SIGNAL |
| --- | --- |
| 2 | GROUND |
| 3 | GROUND |
| 4 | RIGHT SPEAKER OUT SIGNAL |

## ATX-12V Power Connector

This connector supports the ATX power and provides functions such as modem ring on; wake-up LAN and soft power off are supported by mainboard.  (Power source from Mainboard)

- CN1 : Power Connector

| PIN | Description |
| --- | --- |
| 1 | +5V |
| 2 | +5V |
| 3 | +5VSB |
| 4 | +12V |
| 5 | PS_ON |
| 6 | GND |
| 7 | GND |
| 8 | GND |

| CN2 |
| --- |
| PIN | Description | PIN | Description |
| 1 | GND | 2 | GND |
| 3 | +12V | 4 | +12V |

Note: The power from CN2 should support at least 9A current for the use of P4 CPU.  Otherwise, the operation of CPU could be abnormal.  Do not the power with other devices, such as hard disk.  ICP provides cable specifically for such connection at your choice.

## Digital INPUT/OUTPUT Connector

These I/O pins are +12V level with 8mA source-sink capability.

| CN7 |
| --- |
| PIN | Description | PIN | Description |
| 1 | IN0 | 2 | IN1 |
| 3 | IN2 | 4 | IN3 |
| 5 | OUT0 | 6 | OUT1 |
| 7 | OUT2 | 8 | OUT3 |
| 9 | GND | 10 | VCC5 |

## LVDS (CN4) LCD & Inverter (CN5) Connector

- CN4 : LVDS Connector

| PIN | Description | PIN | Description |
| --- | --- | --- | --- |
| 1 | GROUND | 16 | CH2 DATA3- |
| 2 | GROUND | 17 | CH2 CLK+ |
| 3 | CH1 DATA3+ | 18 | CH2 CLK- |
| 4 | CH1 DATA3- | 19 | CH2 DATA2+ |
| 5 | CH1CLK+ | 20 | CH2 DATA2- |
| 6 | CH1 CLK- | 21 | CH2 DATA1+ |
| 7 | CH1 DATA2+ | 22 | CH2 DATA1- |
| 8 | CH1 DATA2- | 23 | CH2 DATA0+ |
| 9 | CH1 DATA1+ | 24 | CH2 DATA0- |
| 10 | CH1 DATA1- | 25 | GROUND |
| 11 | CH1 DATA0+ | 26 | GROUND |
| 12 | CH1 DATA0- | 27 | LCD power |
| 13 | GROUND | 28 | LCD power |
| 14 | GROUND | 29 | LCD power |
| 15 | CH2 DATA3+ | 30 | LCD power |

Please refer to Appendix E for LCD application example.

- CN5 : Inverter Connector

| PIN | Description |
| --- | --- |
| 1 | NC |
| 2 | GROUND |
| 3 | BKL-POWER, 12V |
| 4 | GROUND |
| 5 | +5V |

# 4.		    Award BIOS Setup

## 4.1    Introduction

This chapter discusses the setup program in the BIOS.  It will give users a step-by-step guidance to configure the system.  The user-defined configuration is then stored in the battery-backed CMOS RAM, which retains the customized information while the power is off.

## 4.2    Starting Setup

The BIOS is immediately active when the computer has been turned on. While the BIOS is in control, the setup program will be activated by one of the following ways:

- Press <Del> immediately after switching the system on, or

- Press <Del> when the following message appears at the bottom of the screen during POST (Power On Self-Test):

Press DEL to enter SETUP

If the message passes before the user responds and the user still wants to enter Setup, please turn off the power first and then switch it back on to restart the system; or simply press the "RESET" button on the system case to reboot the system.  The alternative way to restart the system is  simultaneously pressing <Ctrl>, <Alt>, and <Delete> keys.  If the user do not press the keys at the right timing and the system does not boot, an error message will be displayed and the user will be prompted to...

PRESS F1 TO CONTINUE,  DEL TO ENTER SETUP

## 4.3    Using Setup

In general, the arrow keys are used to highlight items, then press <Enter> to select the item. The following table provides more details about how to navigate in the setup program using the keyboard.

| Key | Function |
| --- | --- |
| Up Arrow | Move to the previous item |
| Down Arrow | Move to the next item |
| Left Arrow | Move to the item on the left (menu bar) |
| Right Arrow | Move to the item on the right (menu bar) |
| Esc | Main Menu: Quit without saving changes Submenus: Exit Current page to the next higher level menu |
| Move Enter | Move to the desired item |
| PgUp key | Increase the numeric value or make changes |
| PgDn key | Decrease the numeric value or make changes |
| + key | Increase the numeric value or make changes |
| - key | Decrease the numeric value or make changes |
| Esc key | Main Menu -- Quit and save no changes into CMOS Status Page Setup Menu and Option Page Setup Menu -- Exit current page and return to Main Menu |
| F1 key | General help on Setup navigation keys |
| F5 key | Load previous values from CMOS |
| F6 key | Load the fail-safe defaults from BIOS default table |
| F7 key | Load the optimized defaults |
| F10 key | Save all the CMOS changes and exit |

## 4.4    Main Menu

Once enter the AwardBIOS™ CMOS Setup Utility, the Main Menu will appear on the screen.  The Main Menu allows users to select from several setup functions and two exit choices.  Use the arrow keys to go through the items and press <Enter> to accept and enter the sub-menu.

Phoenix - AwardBIOS CMOS Setup Utility

| Standard CMOS Features Advanced BIOS Features Advanced Chipset Features Integrated Peripherals Power Management Setup PnP/PCI Configurations PC Health Status | Frequency/Voltage Control Load Fail-Safe Defaults Load Optimized Defaults Set Supervisor Password Set User Password Save & Exit Setup Exit Without Saving |
| --- | --- |
| Esc : Quit F9 : Menu in BIOS ( ( ( ( : Select Item F10 : Save & Exit Setup |
| Time, Date, Hard Disk Type…. |

Note: The brief description of each highlighted selection appears at the bottom of the screen.

### 4.4.1 Setup Items

The main menu includes the following main setup categories.  Recall that some systems may not include all entries.

#### Standard CMOS Features

Use this menu for basic system configuration.  See Section 4.5 for the details.

#### Advanced BIOS Features

Use this menu to set the advanced features available on the system.  See Section 4.6 for the details.

#### Advanced Chipset Features

Use this menu to change the values in the chipset registers and optimize the system's performance.  See section 4.7 for the details.

#### Integrated Peripherals

Use this menu to configure all settings for integrated peripherals.  See section 4.8 for the details.

#### Power Management Setup

Use this menu to configure all settings for power management. See section 4.9 for the details.

#### PnP / PCI Configuration

This entry appears if the system supports PnP / PCI.  See section 4.10 for the details.

#### Frequency/Voltage Control

Use this menu to configure all settings for frequency/voltage control.  See section 4.11 for the details.

#### Load Fail-Safe Defaults

Use this menu to load the BIOS default values for the minimal/stable performance for the system to operate.  See section 4.12 for the details.

#### Load Optimized Defaults

Use this menu to load the BIOS default values that are factory settings for optimal system performance.See section 4.12 for the details.

#### Supervisor / User Password

Use this menu to set User and Supervisor Passwords. See section 4.13 for the details.

#### Save & Exit Setup

Save CMOS value changes to CMOS and exit setup.  See section 4.14 for the details.

#### Exit Without Save

Abandon all CMOS value changes and exit setup.  See section 4.14 for the details.

## 4.5    Standard CMOS Setup

The items in Standard CMOS Setup Menu are divided into 10 categories.  Each category includes none, oneore than or m one setup items.  Use the arrow keys to highlight the item and then use the <PgUp> or <PgDn> keys to select the wanted value for each item.

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Standard CMOS Features |
| Date <mm:dd:yy> Wed, Nov 12 2003 Time <hh:mm:ss> 16:19:20 IDE Primary Master HD Model Name IDE Primary Slave <Press Enter> None IDE Secondary Master <Press Enter> None IDE Secondary Slave <Press Enter> None Video EGA/VGA Halt On All, But Keyboard Based Memory 640K Extended Memory 65535K Total Memory 1024K | Item Help Menu Level ( Change the day, month, year and century |
| ((((:Move Enter: Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

Figure 1:  The Main Menu

Main Menu Selections

| Item | Options | Description |
| --- | --- | --- |
| Date | MM : DD : YYYY | Set the system date. |
| Time | HH : MM : SS | Set the system time |
| IDE Primary Master | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Primary Slave | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Secondary Master | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Secondary Slave | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| Video | EGA/VGA CGA 40 CGA 80 MONO | Select the default video device |
| Halt On | All Errors No Errors All, but Keyboard All, but Diskette All, but Disk/Key | Select the situation in which you want the BIOS to stop the POST process and notify you |
| Base Memory | N/A | Displays the amount of conventional memory detected during boot up |
| Extended Memory | N/A | Displays the amount of extended memory detected during boot up |
| Total Memory | N/A | Displays the total memory available in the system |

Table 2 Main Menu Selections

#### IDE Adapters

The IDE adapters control the hard disk drive. Use a separate sub menu to configure each hard disk drive.

Figure 2 shows the IDE primary master sub menu.

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| IDE Primary Master |
| IDE HDD Auto-Detection Press Enter IDE Primary Master Auto Access Mode Auto Capacity 15362 MB Cylinder 29765 Head 16 Precomp 0 Landing Zone 29764 Sector 63 | Item Help Menu Level (( To auto-detect the HDD’s size, head... on this channel |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

Figure 2  IDE Primary Master sub menu

Use the legend keys to navigate this menu. Use Table 3 to configure the hard disk.

| Item | Options | Description |
| --- | --- | --- |
| IDE HDD Auto-detection | Press Enter | Press Enter to auto-detect the HDD on this channel. If detection is successful, it fills the remaining fields on this menu. |
| IDE Primary Master | None Auto Manual | Selecting ‘manual’ lets you set the remaining fields on this screen. Selects the type of fixed disk. "User Type" will let you select the number of cylinders, heads, etc. Note: PRECOMP=65535 means NONE ! |
| Capacity | Auto Display your disk drive size | Disk drive capacity (Approximated). Note that this size is usually slightly greater than the size of a formatted disk given by a disk checking program. |
| Access Mode | CHS LBA Large Auto | Choose the access mode for this hard disk |

Table 3 Hard disk selections

## 4.6    Advanced BIOS Features

This section allows users to configure the system for basic operation.  The options for the system’s default speed, boot-up sequence, keyboard operation, shadowing and security are available.

| Phoenix - AwardBIOS CMOS Setup Utility Software |
| --- |
| Advanced BIOS Features |
| Virus Warning Disabled CPU L1 & L2 Cache Enabled CPU L3 Cache Enabled Quick Power On Self Test Enabled First Boot Device CDROM Second Boot Device HDD-0 Third Boot Device USB-FDD Boot other device Enabled Boot Up NumLock Status On Gate A20 Option Fast Typematic Rate Setting Disabled X Typematic Rate (Chars/Sec) 6 X Typematic Delay (Msec) 250 Security Option Setup APIC Mode Enabled MPS Version Control For OS 1.4 OS Select For DRAM > 64MB Non-OS2 Report NO FDD For Win 95 No | Item Help _____________________ Menu Level ( Allows you to choose the VIRUS warning feature for IDE Hard Disk boot sector protection. If this function is enabled and someone attempt to write data into this area, BIOS will show a warning message on screen and alarm beep |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

#### Virus Warning

Allows users to choose the VIRUS Warning feature for IDE Hard Disk boot sector protection.  If this function is enabled and someone attempts to write data into this area, BIOS will show a warning message on screen and alarm beep will be heard.

| Enabled | Activates automatically when the system boots up causing a warning message to appear when anything attempts to access the boot sector or hard disk partition table. |
| --- | --- |
| Disabled | No warning message will appear when anything attempts to access the boot sector or hard disk partition table. |

#### CPU L1 & L2 Cache

These two categories speed up memory access.  However, it depends on CPU/chipset design.

| Enabled | Enable cache |
| --- | --- |
| Disabled | Disable cache |

#### Quick Power On Self Test

This category speeds up Power On Self Test (POST) after the computer is on.  If it is set to Enable, BIOS will shorten or skip some check items during POST.

| Enabled | Enable quick POST |
| --- | --- |
| Disabled | Normal POST |

#### First/Second/Third/Other Boot Device

The BIOS attempts to load the operating system from the devices in the sequence selected in these items.

The Choice: Floppy, LS120, HDD0-3, SCSI, CDROM, ZIP 100 , LAN, Disabled.

#### Boot Up NumLock Status

Select power on state for NumLock.

The choice: On/Off.

#### Gate A20 Option

Select if chipset or keyboard controller should control GateA20.

| Normal | A pin in the keyboard controller controls GateA20 |
| --- | --- |
| Fast | Lets chipset control GateA20 |

#### Typematic Rate Setting

Key strokes repeat at a rate determined by the keyboard controller.  When enabled, the typematic rate and typematic delay can be selected.

The choice: Enabled/Disabled.

#### Typematic Rate (Chars/Sec)

Sets the number of times a second to repeat a key stroke when the key has been held down.

The choice: 6, 8, 10, 12, 15, 20, 24, 30.

#### Typematic Delay (Msec)

Sets the delay time after the key is held down before it begins to repeat the keystroke.

The choice: 250, 500, 750, 1000.

#### Security Option

Select whether the password is required every time the system boots or only when the user enters setup.

| System | The system will not boot and access to Setup will be denied if the correct password is not entered at the prompt. |
| --- | --- |
| Setup | The system will boot, but access to Setup will be denied if the correct password is not entered at the prompt. |

Note:  To disable security, select PASSWORD SETTING at Main Menu and then the user will be asked to enter password.  Do not type anything and just press <Enter>, it will disable security.  Once the security is disabled, the system will boot and Setup page can be accessed freely.

#### OS Select For  DRAM > 64MB

Select the operating system running with greater than 64MB of RAM on the system.

The choice: Non-OS2, OS2.

#### Report No FDD For Win 95

Whether report no FDD for Win 95 or not.

The choice: Yes, No.

## 4.7    Advanced Chipset Features

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Advanced Chipset Features |
| DRAM Timing Selectable By SPD CAS Latency Time 2.5 Active to Precharge Delay 7 DRAM RAS# to CAS# Delay 3 DRAM RAS# Precharge 3 DRAM Data Integrity Mode Non-ECC MGM Core Frequency Auto Max 266MHz System BIOS Cacheable Enabled Video BIOS Cacheable Disabled Memory Hole At 15M-16M Disabled Delayed Transaction Enabled Delayed Prior to Thermal 16 Min AGP Aperture Size <MB> 64MB ** On-Chip VGA Setting ** On-Chip VGA Enabled On-Chip Frame Buffer Size 32MB Boot Display CRT+LFP Panel Scaling Auto Panel Number 800X600 Flash BIOS Disabled | Item Help _______________________ Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

This section allows users to configure the system based on the specific features of the installed chipset.  This chipset manages bus speeds and accesses to system memory resources, such as DRAM and the external cache.  It also coordinates communications between the conventional ISA bus and the PCI bus.  It must be stated that these items should never need to be altered.  The default settings have been chosen because they provide the best operating conditions for the system.

#### DRAM Timing Selectable

The first chipset settings deal with CPU access to dynamic random access memory (DRAM).  The default timings have been carefully chosen and should only be altered if data is being lost.  Such a scenario might well occur if the system had mixed speed DRAM chips installed so that greater delays may be required to preserve the integrity of the data held in the slower memory chips.

#### CAS Latency Time

When synchronous DRAM is installed, the number of clock cycles of CAS latency depends on the DRAM timing.

The Choice: 1.5 , 2, 2.5, 3

#### DRAM RAS# to CAS#  Delay

- This field lets users insert a timing delay between the CAS and RAS

strobe signals.

- It is used when DRAM is written to, read from, or refreshed.

- Choice 2 means shorter delay which shortens the process of charging; and  choice 3 means longer delay which lengthens the process of charging.

- This field applies only if the synchronous DRAM is installed in the system.

The choice: 2, 3.

#### DRAM RAS# Precharge

If an insufficient number of cycles is allowed for the RAS to accumulate its charge before DRAM refresh, the refresh may be incomplete and the DRAM may fail to retain data. Fast gives faster performance; and Slow gives more stable performance.  This field applies only when synchronous DRAM is installed in the system.

The choice: 2, 3.

#### System BIOS Cacheable

Selecting Enabled allows caching of the system BIOS ROM at F0000h-FFFFFh, resulting in better system performance.  However, if any program writes to this memory area, a system error may result.

The choice: Enabled, Disabled.

#### Video BIOS Cacheable

Select Enabled allows caching of the video BIOS , resulting in better system performance.  However, if any program writes to this memory area, a system error may occur.

The Choice: Enabled, Disabled.

#### Memory Hole At 15M-16M

This area of system memory can be reserved for ISA adapter ROM.  When this area is reserved, it cannot be cached. The user information of peripherals that requests this area of system memory usually discusses their memory requirements.

The Choice: Enabled, Disabled.

#### Delay Transaction

The chipset has an embedded 32-bit posted write buffer to support delay transactions cycles.  Select Enabled to support compliance with PCI specification version 2.1.

The Choice: Enabled, Disabled.

#### AGP Aperture Size (MB)

Select the on-chip video window size for VGA drive use.

The Choice: 4MB, 8MB, 16MB, 32MB, 64MB, 128MB, 256MB

#### On-chip VGA

Enabled/Disabled On-chip VGA

#### Flash BIOS

Disabled/Enabled Flash BIOS

## 4.8    Integrated Peripherals

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Integrated Peripherals |
| (On-Chip IDE Device Press Enter (Onboard Device Press Enter (SuperIO Device Press Enter Onboard Serial Port 3 3E8 Serial Port 3 Use IRQ IRQ10 Onboard Serial Port 4 2E8 Serial Port 4 Use IRQ IRQ11 Onboard Serial Port 5 4F8 Serial Port 5 Use IRQ IRQ10 Onboard Serial Port 6 4E8 Serial Port 6 Use IRQ IRQ11 | Item Help ________________ Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC: Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

Note: There are some item in bottom of scroll.

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| On-Chip IDE Device |
| On-Chip Primary PCI IDE Enabled IDE Primary Master PIO Auto IDE Primary Slave PIO Auto IDE Primary Master UDMA Auto IDE Primary Slave UDMA Auto On-Chip Secondary PCI IDE Enabled IDE Secondary Master PIO Auto IDE Secondary Slave PIO Auto IDE Secondary Master UDMA Auto IDE Secondary Slave UDMA Auto IDE HDD Block Mode Enabled | Item Help ________________ Menu Level ( If your IDE hard drive supports block mode select Enabled for automatic detection of the optimal number of block read/write per sector the drive can support |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC: Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Onboard Device |
| USB Controller Enabled USB 2.0 Controller Enabled USB Keyboard Support Enabled USB Mouse Support Enabled AC97 Audio Auto Onboard/CNR LAN selection Auto Init Display First Onboard/AGP | Item Help ________________ Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC: Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| SuperIO Device |
| Onboard Serial Port 1 3F8/IRQ4 Onboard Serial Port 2 2F8/IRQ3 UART Mode Select Normal UR2 Duplex Mode Half Onboard Parallel Port 378/IRQ7 Parallel Port Mode SPP ECP Mode Use DMA 3 PWRON After PER-Fail Off | Item Help ________________ Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC: Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

#### On-Chip Primary/Secondary PCI IDE

The integrated peripheral controller contains an IDE interface with support for two IDE channels.  Select Enabled to activate each channel separately.

The choice: Enabled, Disabled.

#### IDE  Primary/Secondary Master/Slave PIO

The four IDE PIO (Programmed Input/Output) fields let users set a PIO mode (0-4) for each of the four IDE devices supported by the onboard IDE interface. Modes 0 through 4 provide successively increased performance. In Auto mode, the system automatically determines the best mode for each device.

The choice: Auto, Mode 0, Mode 1, Mode 2, Mode 3, Mode 4.

#### IDE Primary/Secondary Master/Slave UDMA

Ultra DMA-33/66 implementation is possible only if the IDE hard drive supports it and the operating environment includes a DMA driver (Windows 95 OSR2 or a third-party IDE bus master driver). If your hard drive and your system software both support Ultra DMA-33/66, select Auto to enable BIOS support.

The Choice: Auto, Disabled.

#### IDE HDD Block Mode

Block mode is also called block transfer, multiple commands, or multiple sector read/write.  If the IDE hard drive supports block mode (most new drives do), select Enabled for automatic detection of the optimal number of block read/writes per sector the drive can support.

The choice: Enabled, Disabled

#### USB Controller

Select Enabled if the system contains a Universal Serial Bus (USB) controller.

The Choice: Enabled, Disabled.

#### USB Keyboard Support

Select Enabled if the system contains a Universal Serial Bus (USB) controller.

The Choice: Enabled, Disabled.

#### AC97 Audio

This item allows users to decide to Auto/disable the AC97 Audio.

The choice: Enabled, Disabled.

#### Onboard Serial Port 1/Port 2

Select an address and corresponding interrupt for the first and second serial ports.

The choice: 3F8/IRQ4, 2E8/IRQ3, 3E8/IRQ4, 2F8/IRQ3, Disabled, Auto

#### UART Mode Select

Select a serial port 2 operation mode.

The choice: Normal, IrDA, ASKIR, SCR

#### Onboard Parallel Port

Select an address and corresponding interrupt for the parallel ports.

The choice: 378/IRQ7, 278/IRQ5, 3BC/IRQ7,  Disabled,

#### Parallel Port  Mode

Select a parallel operation mode.

The choice: SPP, EPP, ECP,ECP+EPP

#### Onboard Serial Port 3/ 4/ 5/ 6

Select an address for the serial ports.

The choice: 3E8/ 2E8/ 4F8/ 4E8

#### Serial Port 3/ 4/ 5/ 6 Use IRQ

Select a corresponding interrupt for the serial ports.

The choice: IRQ10 /11

## 4.9    Power Management Setup

The Power Management Setup allows the user to configure the system to the most effective energy save.

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Power Management Setup |
| ACPI Function Enabled ACPI Suspend Type S1<POS> X Run VGABIOS if S3 Resume Auto Power Management User Define Video Off Method DPMS Video Off In Suspend Yes Suspend Type Stop Grant Suspend Mode Disabled HDD Power Down Disabled Soft-Off by PWR-BTTN Instant-Off Power On by Ring Enabled X USB KB Wake-Up From S3 Disabled Resume by Alarm Disabled X Date(of Month) Alarm 0 X Time(hh:mm:ss) Alarm 0 : 0 : 0 ** Reload Global Timer Events ** Primary IDE 0 Disabled Primary IDE 1 Disabled Secondary IDE 0 Disabled Secondary IDE 1 Disabled FDD,COM,LPT Port Disabled PCI, PIRQ[A-D]# Disabled | Item Help _______________________ Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

#### Power Management

This category allows the user to select the type (or degree) of power saving related to the following modes:

- HDD Power Down

- Doze Mode

- Suspend Mode

There are four selections for Power Management, three of which have fixed mode settings.

| Disable (default) | No power management. Disables all four modes |
| --- | --- |
| Min. Power Saving | Minimum power management Doze Mode = 1 hr. Standby Mode = 1 hr. Suspend Mode = 1 hr. HDD Power Down = 15 min. |
| Max. Power Saving | Maximum power management -- ONLY AVAILABLE FOR SL CPU’s Doze Mode = 1 min. Standby Mode = 1 min. Suspend Mode = 1 min. HDD Power Down = 1 min. |
| User Defined | Allows the user to set each mode individually. If it’s not disabled, each of the ranges is from 1 min. to 1 hr. except for HDD Power Down whose ranges from 1 min. to 15 min. and disable. |

#### Video Off Method

This determines the manner of how the monitor becomes blank.

| V/H SYNC+Blank | This selection will cause the system to turn off the vertical and horizontal synchronization ports and write blanks to the video buffer. |
| --- | --- |
| Blank Screen | This option only writes blanks to the video buffer. |
| DPMS | Initial display power management signaling. |

#### Video Off In Suspend

This determines the manner in which the monitor is blanked.

The choice: Yes, No.

#### Suspend	Type

Defines the Suspend Type.

The choice: PWRON Suspend, Stop Grant.

#### Suspend Mode

If it’s enabled and the power save time of system has met, all devices except the CPU will be shut off.

The choice: 1Min, 2Min, 4Min, 8Min, 12Min, 20Min, 30Min, 40Min, 1Hour, Disabled.

#### HDD Power Down

When enabled and after the set time of system inactivity, the hard disk drive will be powered down while all other devices remain active.

The choice: 1Min, 2Min, 3Min, 4Min, 5Min, 6Min, 7Min, 8Min, 9Min, 10Min, 11Min, 12Min, 13Min, 14Min, 15Min, Disabled.

#### PM EVENTS

PM events are I/O events whose occurrence can prevent the system from entering a power saving mode or can awaken the system from such a mode.  In effect, the system remains alert for anything which occurs to a device which is configured as Enabled , even when the system is in a power down mode.

Primary IDE 0

Primary IDE 1

Secondary IDE 0

Secondary IDE 1

FDD, COM, LPT Port

PCI PIRQ[A-D] #

## 4.10    PnP/PCI Configuration Setup

This section describes configuring the PCI bus system.  PCI stands for Personal Computer Interconnect. It is a system which allows I/O devices to operate at speeds nearing the speed the CPU itself uses when communicating with its own special components.  This section covers some specific technical settings and it is strongly recommended that only experienced users should make any changes to the default settings.

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| PnP/PCI Configurations |
| Reset Configuration Data Disabled Resources Controlled By Auto(ESCD) X IRQ Resources Press Enter PCI/VGA Palette Snoop Disabled | Item Help ------------------------- Menu Level ( Default is Disabled. Select Enabled to reset Extended System Configuration Data(ESCD) when the user exits Setup if you have installed a new add-on and the system reconfiguration has caused such a serious conflict that the OS cannot boot |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC: Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

#### Reset Configuration Data

In most cases, this field is set to “Disabled.” Select Enabled to reset Extended System Configuration Data (ESCD) when you exit Setup if you have installed a new add-on and the system reconfiguration has caused such a serious conflict that the operating system can not boot.

The choice: Enabled, Disabled.

#### Resource controlled by

The Award Plug and Play BIOS has the capacity to automatically configure all of the boot and Plug and Play compatible devices.  However, this capability means absolutely nothing unless the user is using a Plug and Play operating system such as Windows(95.  If the option “Manual” is selected, the user can choose a specific resources from the sub-menu.

The choice: Auto(ESCD), Manual.

#### IRQ Resources

When resources are controlled manually, assign each system interrupt a type based on the type of interrupt the device uses..

#### IRQ3/4/5/7/9/10/11/12/14/15 assigned to

This item allows the user to determine the IRQ assigned to the ISA bus and is not available to any PCI slot. Legacy ISA for devices compliant with the original PC AT bus specification, PCI/ISA PnP for devices compliant with the Plug and Play standard whether designed for PCI or ISA bus architecture.

The choice: PCI Device, Reserved.

#### PCI/VGA Palette Snoop

Leave this field disabled.

The choice: Enabled, Disabled.

## 4.11    PC Health Status

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| PC Health Status |
| Shutdown Temperature Disabled VCORE 1.44V VTT 1.48V +3.3V 3.26V +5.0V 4.95V +12V 11.58V +5VSB 4.89V Voltage Battery 3.12V SYSTEM Temperature 25°C CPU Temperature 37°C Fan 1 Spend 5443 Fan 2 Spend 0 | Item Help ------------------------- Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

Note: Normal CPU Fan RPM is over than 5000 RPM. If the CPU Fan RPM is less than that figure, it means something is wrong and the CPU will be in an overheat condition. Make sure that the connection at Fan1/Fan2 is correct.

## 4.12    Frequency/Voltage Control

| Phoenix - AwardBIOS CMOS Setup Utility |
| --- |
| Frequency/Voltage Control |
| CPU Clock Ratio 8 X Auto Detect PCI Clk Enabled Spread Spectrum Disabled | Item Help ------------------------- Menu Level ( |
| ((((:Move Enter:Select +/-/PU/PD:Value F10:Save ESC:Exit F1:General Help F5:Previous Values F6:Fail-safe defaults F7:Optimized Defaults |

#### Auto Detect PCI Clk

This item allows the user  to enable/disable auto detect DIMM/PCI Clock.

The choice: Enabled, Disabled.

#### Spread Spectrum

This item allows the user to enable/disable the spread spectrum modulate.

The choice: Enabled, Disabled.

## 4.13    Defaults Menu

Selecting “Defaults” from the main menu will bring up the two options described below

Load Fail-Safe Defaults

If  the user presses <Enter> on this item, a dialog box with a message similar to the following will pop up:

Load Fail-Safe Defaults (Y/N) ?  N

Pressing ‘Y’ loads the BIOS default values for the most stable, minimal-performance system operations.

Load Optimized Defaults

If the user presses <Enter> on this item, a dialog box with a message similar to the following will pop up:

Load Optimized Defaults (Y/N) ?  N

Pressing ‘Y’ loads the default values that are factory settings for optimal performance system operations.

## 4.14    Supervisor/User Password Setting

The user can set the password for either supervisor or user,, or for both of them.

supervisor password: for entering and changing the settings of the     system

user password: for just entering the system but does not have the privilege to change any settings of the system

If this function is enabled, the following message will appear to guide the user to create a 								password.

ENTER PASSWORD:

Type the password, up to eight characters in length, and press <Enter>.  The password typed now will clear any previously entered password from CMOS memory.  The user will be asked to re-type the password, and press <Enter>.

Note: The user may press <Esc> to skip the selection and not to enter a   password.

To disable a password, just press <Enter> when prompted to enter the password. Once the password is disabled, the system will boot and the user can enter Setup freely.

PASSWORD DISABLED:

When a password has been set, the user will be prompted to enter it every time when entering Setup.  This prevents an unauthorized user from changing any part of the system configuration.

Additionally, when a password is set, the user can also require the BIOS to request a password every time the system starts.  This would prevent any unauthorized use of the computer.

The user determines when the password is required within the BIOS Features Setup Menu and its security option (see Section 3).  If the security option is set to “password”, then it will be required both at boot and at entry to Setup.  If it is set to “Setup”, the password is needed only when trying to enter Setup.

## 4.15    Exit Selecting

### Save  & Exit Setup

Pressing <Enter> on this item asks for confirmation:

Save to CMOS and EXIT (Y/N)?  Y

Pressing “Y” stores the selections made in the menus in CMOS – a special section of memory that stays on after the system has been turned off.  When the computer reboots again, the BIOS configures the system according to the Setup selections stored in CMOS.

### Exit Without Saving

Pressing <Enter> on this item asks for confirmation:

Quit without saving (Y/N)?  Y

This allows the user  to exit Setup without saving any changes in CMOS.  The previous selections remain in effect. This exits the Setup utility and restarts the computer.

# Appendix A: Watchdog Timer

The Watchdog Timer is provided to ensure that standalone systems can always recover from catastrophic conditions that cause the CPU to crash. This condition may have occurred by software bug. When the CPU stops working correctly, hardware on the board will either perform a hardware reset (cold boot) to bring the system back to a known state.

A BIOS function call (INT 15H) is used to control the Watchdog Timer:

INT 15H:

AH – 6FH

Sub-function: AL – 2 : Set the Watchdog Timer’s period BL : Time-out value(Its unit--second or minute, is dependent on the item “Watchdog Timer unit select” in CMOS setup).

You have to call sub-function 2 to set the time-out period of Watchdog Timer first. If the time-out value is not zero, the Watchdog Timer will start counting down. While the timer value reaches zero, the system will reset. To ensure that this reset condition does not occur, the Watchdog Timer must be periodically refreshed by calling sub-function 2. However the Watchdog timer will be disabled if you set the time-out value to be zero.

A tolerance of at least 10% must be maintained to avoid unknown routines within the operating system (DOS), such as disk I/O that can be very time-consuming.

Note: when exiting a program it is necessary to disable the Watchdog Timer, otherwise the system will reset.

Example program:

; INITIAL TIMER PERIOD COUNTER

;

W_LOOP:

MOV     AX, 6F02H              ;setting the time-out value

MOV     BL, 30                     ;time-out value is 48 seconds

INT       15H

;

; ADD YOUR APPLICATION PROGRAM HERE

;

CMP      EXIT_AP, 1            ;is your application over?

JNE       W_LOOP               ;No, restart your application

MOV    AX, 6F02H              ;disable Watchdog Timer

MOV    BL, 0                        ;

INT      15H

;

; EXIT

;

# Appendix B: I/O Address Map

- I/O Address Map

| I/O Address Map | Description |
| --- | --- |
| 000-01F | DMA Controller #1 |
| 020-021 | Interrupt Controller # 1, Master |
| 040-05F | System Timer |
| 060-06F | Standard 101/102 keyboard Controller |
| 070-07F | Real time Clock, NMI Controller |
| 080-0BF | DMA Page Register |
| 0A0-0BF | Interrupt Controller # 2 |
| 0C0-0DF | DMA Controller # 2 |
| 0F0-0F0 | Clear Math Coprocessor Busy |
| 0F1-0F1 | Reset Math Coprocessor |
| 0F8-OFF | Math Coprocessor |
| 170-1F7 | BUS Master PCI IDE Controller |
| 201 | DIO |
| 278-27F | Parallel Printer Port 2 |
| 2E8-2EF | Serial Port 4 |
| 2F8-2FF | Serial Port 2 |
| 376-376 | BUS Master PCI IDE Controller |
| 378-37F | Parallel Printer Port 1 |
| 3B0-3DF | Intel 82852GM/GME Graphic Controller |
| 3E8-3EF | Serial Port 3 |
| 3F0-3F7 | Floppy Disk Controller |
| 3F8-3FF | Serial Port 1 |
| 4F8-4FF | Serial Port 5 |
| 4E8-4EF | Serial Port 6 |
| 480-48F | PCI BUS |

- 1st MB Memory Address Map

| Memory address | Description |
| --- | --- |
| 00000-9FFFF | SYSTEM MEMORY |
| A0000-BFFFF | VGA BUFFER |
| C0000-CFFFF | VGA BIOS |
| E0000-FFFFF | SYSTEM BIOS |
| 100000 | EXTEND MEMORY |

- IRQ Mapping Chart

| IRQ0 | System Timer | IRQ8 | RTC clock |
| --- | --- | --- | --- |
| IRQ1 | Keyboard | IRQ9 | AC97 AUDIO |
| IRQ2 | IRQ Controller | IRQ11 | COM4 |
| IRQ3 | COM2 | IRQ10 | COM3 |
| IRQ4 | COM1 | IRQ12 | PS/2 mouse |
| IRQ5 | PCI DEVICES | IRQ13 | FPU |
| IRQ6 | COM5/6 | IRQ14 | Primary IDE |
| IRQ7 | Printer | IRQ15 | Secondary IDE |

- DMA Channel Assignment

| Channel | Function |
| --- | --- |
| 0 | Available |
| 1 | Available |
| 2 | Available |
| 3 | Available |
| 4 | Cascade for DMA controller 1 |
| 5 | Available |
| 6 | Available |
| 7 | Available |

# Appendix C: How to use Wake-Up Function

NOVA-4710 provides two kinds of Wake up Function.

This page describes how to use Modem Wake-Up and LAN Wake-Up function.

Wake-Up function is enabled when you use ATX power supply.

Wake–Up On Modem (Ring):

You must set the option Resume on Ring of CMOS SETUP to enable this option.  The ATX power supply will be switched on when there is a ring signal detected on pin “RI” of serial port.

Wake-Up On LAN:

You must set the option Resume on LAN of CMOS SETUP to enable this option.

When your computer is turned off while LAN Link/Active LED is flashing, it indicates that LAN chip has entered standby mode and waits for Wake-Up signal.  You can use other computers to wake up your computer by sending ID to it.

ID: ID is the address of your system LAN.  Every LAN chip has a factory-set ID, which can be found from network information in WINDOWS.

ID’s format is xxxxxxxxxxxx

Example ID: 009027388320